## Slide 1: ZKI
Hands-On training
Elisa Schröter, Ralph Kiefl
10.04.2019 – The Hague

## Slide 2: Airborne and Terrestrial Situational Awareness
BackgrounD DLR Solution
Ground Station &
Processing Unit
Camera System
Terrestrial Traffic Sensors
Dissemination, Visualisation & Interaction
Image Data Link
C³ Data Link
Ground Control Station U-Fly
Command & Control
training session
Module: ZKI

## Slide 3
DLR user Service ZKI (Center for Satellite based Crisis information)
Provides information layers (e.g. actual water mask) and ready to use 2D / 3D maps
    For large scale events
    For professional responders
Deployed in the response phase
… to assess disaster extent
… to support damage assessment
… to contribute to COP (e.g. tools such as LCMS, Crisis Suite)
… to support decision making (e.g. tools such as KeepOperational)
ZKI OVERVIEW
Main Features for Trial 4

## Slide 4: ZKI OVERVIEW
Services & Products for Trail 4
Preparation of crisis related information
  water mask derived from remote sensing data
  In this Trial: simulated water mask, as if derived from aerial imagery and
  processed based on DLR user service ZKI processing facilities
Web based Product Dissemination
  OGC WMS / WFS web services for water mask
  Download service for ready to use map products
Generation of ready to use maps
  2D GeoPDF
  3D PDF

## Slide 5: ZKI Hands-on Training
COntent
When and how to activate ZKI and receive mapping products
Accessing web services for actual water masks
Accessing and working with ZKI 2D GeoPDF map documents
Accessing and working with ZKI 3D PDF map documents

## Slide 6: ZKI Hands-on Training
WHEN to activate
Preparation/ Prevention
Alertness*
Risk Analysis
Emergency Relief
Reconstruction
Transition Phase Relief and Reconstruction
Disaster event
As soon as
IMMINENT THREAT is known
>>> send request to ZKI asap

## Slide 7: ZKI Hands-on Training
Request Email
How to activate
Who activates (inquiring authority and contact person)
Type of event (natural disaster / police investigation / …)
Product type (satellite imagery or aerial imagery / disaster extent analysis / …)
Product format (WMS / WFS layer for COP tools / map product)
Delivery date (fast mode - as soon as possible - / date: … )
Area of interest (name of location)
Additional comments/requests
Please send the request Email to Trial Email Account „ZKI“. if you have any questions in advance oR need Consultation on your inquiry please call +49 8153 28 44 33 88

## Slide 8: ZKI Hands-on Training
OGC Web Map Service (WMS): Viewing service https://www.opengeospatial.org/standards/wms
Used for visual overlay other layers in map applications (e.g. LCMS, Crisis Suite)
Provides rendered and geo-registered images of geodata
Supports different projections and file formats
Request-Parameters: Layer, area of interest, size, image format, spatial reference
OGC Web Feature Service (WFS): Data service for vector data https://www.opengeospatial.org/standards/wfs
Accessed for further geoprocessing (e.g. KeepOperational, GIS applications)
Supports different projections and file formats
Request-Parameters: Layer, area of interest, file format, spatial reference
Accessing web services for actual water masks

## Slide 9: ZKI Hands-on Training
Accessing web services for actual water masks
https://geoservice.dlr.de/eoc/zki/service/driver/wms? | 
Service | WMS
Request | GetMap
Layers | driver:dryrun1_watermask_tsx_sim
AOI LL | 4.2318027°E 51.962462°N
AOI UR | 4.395028°E 52.113057°N
Image Width | 951
Image Height | 878
Spatial Reference | 4326 Geogr./ WGS84
Format | PNG
Please Open Shortlink: http://s.dlr.de/250h

## Slide 10: ZKI Hands-on Training
Accessing web services for actual water masks
Please Open Shortlink: http://s.dlr.de/mh8c
https://geoservice.dlr.de/eoc/zki/service/driver/wms? | 
Service | WMS
Request | GetMap
Layers | driver:dryrun1_watermask_tsx_sim
AOI LL | 75572 442084
AOI UR | 87017 458670
Frame Width | 1024
Frame Height | 768
Spatial Reference | 28892 (Amersfoort / RD New)
Format | application/openlayers

## Slide 11: ZKI Hands-on Training
https://geoservice.dlr.de/eoc/zki/service/driver/wms? | 
Service | WMS
Request | GetMap
Layers | driver:dryrun1_watermask_tsx_sim
AOI LL | 75572 442084
AOI UR | 87017 458670
Frame Width | 1024
Frame Height | 768
Spatial Reference | 28892 (Amersfoort / RD New)
Format | application/openlayers
Accessing web services for actual water masks
Demo watermask service layer displayed in LCMS (image provided by TNO)

## Slide 12: ZKI Hands-on Training
Accessing web services for actual water masks
Demo watermask service layer displayed in CrisisSuite (image provided by MERLIN)

## Slide 13: ZKI Hands-on Training
Accessing and working with ZKI 2D GeoPDF map documents
Open & access toolbars
Toggle map layers for custom map view
Make messurements
Make comments
Access attribute information
Please use Shortlink
http://s.dlr.de/2968
Download and open FILE:
DRIVER-Exp44_GeoPDF_Magdeburg.pdf

## Slide 14: ZKI Hands-on Training
Accessing and working with ZKI 3D PDF map documents
Open & access toolbars
Navigate through 3D environment
Toggle map layers for custom map view
Make messurements
Make comments
Access attribute information
Please use Shortlink
http://s.dlr.de/m878
Download and open FILE:
DRIVER-Exp44_3D_PDF_Magdeburg.pdf

## Slide 15
zki@dlr.de
www.zki.dlr.de